# Overview
The product is called jigbox until someone comes up with a better name; which will probably take less than 5 minutes because I am not good at thinking up cool names.
# Firmware architecture
Using MIDI as a guide seems like a reasonable starting point as MIDI already has definitions for
1. when a sound starts
2. when the sound stops
3. what the sound is (waveform)
4. Volume
5. Lots of timing information include synchronization, bars and frames within the bar, and metronome types of information
The MIDI communications format is very compact and was designed by musicians so there is probably a lot in there that I could learn from.
There would be 5 voices tied to the 5 buttons. Each voice can be a simple sine wave to test. Later on the voices can be recorded sounds from the microphone, voices created by other uses and share over the wireless, or downloaded from a PC.
Internally I need one buffer per voice. The format will initially be a raw waveform in a format suitable for direct output to the audio out section (probably just an array of 16 bit DAC values for the PWM output).
The audio firmware should copy buffers to the audio out section. The audio out will later need to mix the 5 voices together to get the final DAC value, then convert that to registers for the PWM output. Also the sound may need to be mixed with the metronome output.

Will use the MapleLabs drivers instead of the IAR drivers for accessing the micro-controller peripherals.
Will use the state-machine framework from Quantum Leaps.

# Playing sounds
The USB audio device allow for data to be sent in a usb packet then played through the audio out. Using the code in the file audio_class.c the function that normally starts a buffer playing is
AudioInHandler( )
Create a new function that does not require the USB packet but performs the same basic operations as AudioInHandler and it should play the buffer. A buffer must be created and filled with wav data.

# Other random thoughts

I would like to get the functions working in this order
1. Make a beep. Without this we have little to demo in the final video
2. Make the buttons do something. I would guess the five notes ABCDEF would initially map one-to-one to the buttons.
3. Radio link to a second unit
4. Flash the LED as a metronome.
5. Record from microphone
6. Pitch bending using accelerometers

Task-list in order
1. create some sort of framework and main.c that everyone can start to build off of. We need to stand a fighting chance of merging this stuff together at the end.
2. Make main read the buttons, store the notes in memory and have the AudioOut driver read the notes and play them
3. Radio ????
4. Make a metronome that initially is just 4/4 timing at 100 beats per minute. Look at how MIDI defines the bars and frames.
5. Flash the LED
Modify the conections.odf to include the audio out is on PA8/USART1_CK/TIM1_CH1/MCO

Use maple from leaf labs to and git hub to be our low level library.
Use the QP state-machine framework for the OS

# Link farm
UM0919 is the data sheet for the Discovery board.
http://www.st.com/internet/com/TECHNICAL_RESOURCES/TECHNICAL_LITERATURE/USER_MANUAL/CD00267113.pdf

Maplelabs web page www.leaflabs.com
Maplelabs git repo https://github.com/leaflabs/libmaple
Quantum Leaps (www.state-machine.com)

St micro info:
Value-line discovery board homepage http://www.st.com/internet/evalboard/product/250863.jsp
Value-line user manual CD00267113.pdf